Biohazardous Spill Procedure (example)

- Notify all persons within the laboratory of the spill.

  - Inspect people within the laboratory for visible signs of contamination

  - If contamination is on lab coat only, change lab coats immediately, placing the contaminated lab coat in a biohazard bag for decontamination.

  - If contamination is on hands and arms, gloves are to be removed and hands thoroughly washed with med shield, hibiclens or chlorhexidine, and dried with absorbent paper towel.

  - If contamination is through lab coat, and clothing, then lab manager is to be called immediately for further action.

- Protect Yourself

  - Wear 2 pairs for gloves and safety goggles, and remove spill kit supplies from storage container. (Container, bio hazard bags, dustpan etc).

- Contain & secure

  - Surround the spill with absorbent material, overlay with paper towel or vermiculite

  - Cordon off the area, prevent others from walking through the spill

- Disinfect the spill

  - Apply the appropriate disinfectant (e.g. bleach, virkon, F10)

  - Allow to stand for an appropriate length of time (see directions for that disinfectant – usually 10 minutes for bleach)

- Clean up & dispose of the debris

  - Use tongs, scraper, cardboard or dustpan to remove any sharps, place in sharps container. Avoid using your hands

  - Remove the absorbent material by using a dust pan and deposit in a biohazard bag along with the dust pan.

  - Spray the area with disinfectant and allow a further 10 minutes contact time

  - Remove any residual disinfectant with paper towels. Dispose towels in the biohazard bag.

- Treat any contaminated equipment, and utensils.

  - Spray with disinfectant and allow a 10 minute contact time

  - Remove contamination by wiping down with absorbent material.

  - Repeat above two steps (spray & wipe down)

  - Dispose of used absorbent material in a biohazard bag.

- Clean yourself

  - Remove outer pair of gloves only and dispose in the biohazard bag.

  - Remove goggles and clean with 70% ethanol and wipe clean.

  - Inspect the area again for any missed items or areas of contamination.

  - Remove inner gloves and place them in the biohazard bag.

  - Close biohazard bag and dispose as biohazardous waste.

  - Wash your hands with med shield, hibiclens or chlorhexidine and dry thoroughly

  - Decontaminate your labcoat if required – i.e. dump in a bucket of bleach OR autoclave it

- Return spill kit, and report incident, making sure the spill kit is restocked.

# Text boxes

PLEASE TAKE NOTE:

- Only persons trained in the use of spill kits can clean up spills more than 100ml.

- If spill is more than 1litre, place a Do not enter sign in the entrance door to the laboratory and alert the laboratory manager immediately

  - Tell the laboratory manager of any hazardous information of the material involved in the spill.

- For high risk spills (e.g. infectious or GM biological in risk group 2) do not enter the room for 30mins to allow aerosols to settle